## Slide 1
Object Sorting Machine
Color-Based
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 2
Abstract
Color-based object sorting plays a crucial role in industrial automation, enabling fast and efficient classification of items based on their color properties. The proposed system detects object colors using a TSC34725 color sensor, Arduino Uno microcontroller, Bluetooth module, servo motor, LCD with I2C, and a buzzer to achieve seamless operation and real-time monitoring. This approach enhances automation efficiency in industries such as waste management, food processing, and packaging.
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 3
Introduction
Automation has revolutionized industries by enhancing efficiency and precision. In many sectors, such as manufacturing and recycling, color-based object sorting plays a vital role in classification and quality control. Traditional manual sorting is often slow and error-prone, making automation a more effective solution.
A Color-Based Object Sorting Machine uses color sensors to detect object colors and a microcontroller to process the data, and sorting colors. This system improves speed, accuracy, and reduces human involvement.
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 4
System Model & Block Diagram
  Color Detection: The TSC34725 color sensor detects the color of an object placed in the sorting area.
  Data Processing: The Arduino Uno processes the color data and determines the appropriate bin for the object.
  Sorting Mechanism: The servo motor moves to direct the object to the correct bin based on the processed color data.
  Display and Notification: The LCD displays the number of objects sorted and their colors. The mobile app provides real-time updates and notifications.
  Control Modes:
    Automatic Mode: The system sorts objects continuously until all objects are checked. Upon completion, the buzzer sounds, and a notification is sent to the mobile app.
Manual Mode: Users can specify a number of objects with a specific color on the mobile app. The system stops sorting, activates the buzzer, and sends a notification when the specified number is reached.

## Slide 7
Arduino Uno R3
  Microcontroller: ATmega328P
  Used for: Robotics, home automation, sensor-based systems
  Supports: Digital & analog I/O, PWM, serial communication
Main Specifications:
  Power Supply: 7-12V (VIN) or 5V via USB
  Pins:
  Digital I/O: 14 pins (0-13, 6 support PWM)
  Analog Inputs: 6 pins (A0-A5)
  USB Port: For programming & power
  Reset Button: Restart the board easily
Power & Connectivity
  Prototyping electronic projects
  Interfacing with sensors, motors, displays
  Ideal for beginners & advanced users
Applications:
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 8
TSC34725 Color Sensor
  Function: Detects and measures RGB (Red, Green, Blue) and clear light
  Applications: Color recognition, ambient light sensing, display calibration
  Compatible with: Microcontrollers like Arduino, NodeMCU
Main Specifications:
  VCC: Connects to 3.3V or 5V power
  GND: Connects to ground
  SDA (Serial Data): Connects to the microcontroller's SDA pin
  SCL (Serial Clock): Connects to the microcontroller's SCL pin
  INT (Interrupt): Signals when light levels exceed set thresholds
  LED: Controls onboard illumination (if available)
Pin Configuration:
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 9
Bluetooth Module HC-05
  Operating Voltage: 3.3V - 5V
  Operating Modes: Master & Slave
  Range: Up to 10 meters
  Default Password: 1234 or 0000
  VCC, GND – Power supply.
  TX, RX – Serial communication (UART).
  EN/KEY – Mode configuration switch.
  STATE – Connection status indicator.
Main Specifications:
  Supports both master and slave modes
  LED indicators for connection status
  Supports serial communication with microcontrollers like Arduino, ESP32, and Raspberry Pi
Key Features:
  Wireless data transfer between microcontrollers
  Home automation and IoT projects
  Remote control systems
  Wireless robotics and communication
Applications:
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 10
Servo Moto
  Operating Voltage: Typically 4.8V - 7.4V (depending on model)
  Control Signal: PWM (Pulse Width Modulation)
  Standard Seravo: 0° to 180°
  Continuous Servo: 360° rotation
  Response Time: Fast and precise positioning
Main Specifications:
  Precise angular position control
  Requires only one PWM pin for control
  Available in standard (position control) and continuous rotation (speed control) types
  Compatible with microcontrollers like Arduino, ESP32, Raspberry Pi
Key Features:
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài
  Robotics and automation
  RC cars, drones, and airplanes
  Smart home projects (e.g., automated doors, camera gimbals)
  Industrial automation and prosthetics
Applications

## Slide 11
LCD with I2C
  Interface: I2C
  Operating Voltage: 5V
  GND – Ground pin (connects to Arduino's GND)
  VCC – Power supply pin (usually 5V)
  SDA – Serial Data Line for I2C (connects to Arduino's SDA, usually A4)
  SCL – Serial Clock Line for I2C (connects to Arduino's SCL, usually A5)
Main Specifications:
  Reduces the number of required microcontroller pins (only uses SDA & SCL)
  Supports multiple I2C addresses for flexibility
  Easy to use with libraries like LiquidCrystal_I2C in Arduino
Key Features:
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài
  Displaying sensor readings
  User interfaces for embedded systems
  IoT and automation projects
  Menu-based navigation systems
Applications:

## Slide 12
Buzzer
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài
  Operating Voltage: Typically 3V - 12V
  Current Consumption: ~5mA - 30mA
  Sound Level: ~85dB at 10cm
  VCC (+) – Power supply (3.3V - 5V)
  GND (-) – Ground (GND)
  I/O (Signal) – Receives control signal (from a microcontroller like Arduino)
Main Specifications:
  Simple control with digital HIGH/LOW (Active Buzzer)
  Can generate different tones using PWM (Passive Buzzer)
  Compact and low power consumption
Key Features:
  Alarms and security systems
  Sound notifications in embedded systems
  Timers and reminders
  Electronic toys and smart home devices
Applications:

## Slide 13
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt

## Slide 14
ID | NAME | Contribution
SE181760 | Nguyễn Tuấn Tú | 25% Program Bluetooth, Servo Moto, LCD with I2C, Buzzer, design, Write report and prepare Presentation
SE185022 | Trần Hoàng Tín | 25% Program Arduino, TSC34725 Color Sensor, Software Programing, design and prepare Presentation
SE184132 | Trần Thanh Hoài | 25% Abstract, Introduction, Software Programing, design and prepare Presentation
SE184970 | Nguyễn Tiến Đạt | 25% System Model and Block Diagram, Programing Flowchart, design and prepare Presentation
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài

## Slide 15
Thank
You.
You.
Thank
You.
Thank
Trần Hoàng Tín
Group 4
Nguyễn Tuấn Tú
Nguyễn Tiến Đạt
Trần Thanh Hoài